# Benzene Line Specification: List of Equipment

### Benzene Line for Chemical Preparation of samples for 14C measurement by Liquid Scintillation Counting (LSC) includes:

| Description | Quantity |
| --- | --- |
| Benzene Line |  |
| 1 Charring equipment |  |
| 1.1. A vertical furnace (1100 watt, 220 volt, up to 1250 oC ) | 1 |
| 1.2. Stainless steel reaction vessels with cover (3 small, 2 middle, 1 large and 1 perfored). | 1 |
| 1.3. Thermo-destruction gas utilizing reactor. | 1 |
| 1.4. A mounting for cooling and holding reaction vessels. | 1 |
| 2 The equipment for lithium carbide production of any kind of sample material |  |
| 2.1. A vertical furnace (1100 watt, 220 volt, up to 1250 oC ) | 2 |
| 2.2. An easily discountable water-cooled hermetized head | 1 |
| 2.3. Stainless steel cylindrical reaction vessels (5 small , 8 middle and 2 large ) | 15 |
| 2.4. Titanium liners | 10 |
| 2.5. Special metal stand with a holder for mounting a vacuum gauge with valves for vacuum, argon and carbon dioxide, with fast cooling system for reactor vessels and with seats for storing clean reactor vessels | 1 |
| 2.6. Stainless steel holders ( 15 of different sizes ) and vacuum thermo-destruction technology | 15 |
| 2.7. An auxiliary equipment. | 1 |
| 3. The equipment for lithium carbide production of carbon dioxide and charcoal |  |
| 3.1. CO2 carbide reaction vessels (5 reactors) | 5 |
| 3.2. A holder for mounting a vacuum gauge with valves for vacuum, argon and carbon dioxide, with cryogenic-trap for carbon dioxide with quickly weigh system. | 4 |
| 3.3. An auxiliary equipment. | 1 |
| 4. The equipment for acetylene production. |  |
| 4.1. A lithium carbide hydrolysis module large | 2 |
| 4.2. A lithium carbide hydrolysis module special for micro-samples | 2 |
| 4.3. The equipment for chemical purification and catching of acetylene | 1 |
| 4.4. The equipment for chemical purification and catching of acetylene, adopted for micro-samples. | 1 |
| 5. The equipment for benzene synthesis. |  |
| 5.1. Benzene synthesis system (2 modules). The one module consists of: two vacuum manifolds with gauges, Teflon valves, cryogenic traps, reaction vessel with catalyst, heater-cooler system with temperature controller/ | 2 |
| 5.2. The glass benzene recovery vials with Teflon caps for refining and storage of benzene ( 70 vessels of different sizes ) | 1 |
| 6. The equipment for benzene purification by sublimation. |  |
| 6.1 One vacuum manifolds with gauges, Teflon valves and cryogenic traps. | 1 |
| 6.2. System for fast remove of the Radon | 1 |
| 7. Vials for long time precise measurement |  |
| 7.1. 1,5 ml, 3 ml, 7ml. Each vial consists of Teflon ampoule, titanium holder, titanium spring, Teflon cap with pin valve. | 30 |
| 8. Sets of manuals in English | 1 |
| 9. On-site installation of equipment and training to the end-user staff. benzeneline@gmail.com |  |

### An Offer: Benzene line: equipment, technology, Set-Up & Staff training.

### Benzene line : Equipment for carbon dating : Modern technology : Laboratory SetUp : Training of staff

Copyright © 2013 - 2013 Michael Buzinny 
Page last saved at: 05/12/2013

Benzene line, Radio Carbon Dating Equipment